LCISD will evaluate Proposals for the following services.  Responses will be accepted on individual items.  Vendors are not required to bid on all services.  The following service pricing is requested:

- The awarded vendor will complete a district walkthrough and survey to develop final design drawings, bill of materials and Scope of Work.

  - 1341 classrooms

  - 110 portables

- Vendor will purchase and install new and existing Projectors with rapid-run cabling between projectors and presentation station (approx 862)

  - 613 classrooms

  - 154 classrooms requiring surface mount raceway

  - 90 portables

  - 5 portables requiring surface mount raceway

| Projectors | Classrooms | Classroom with Surface Mount raceway | Portables | Portable with surface mount raceway | Totals |
| --- | --- | --- | --- | --- | --- |
| #2 New | 613 | 154 | 90 | 5 | 862 |
| #4 Existing | 153 | 15 | 1 | 1 | 170 |
| Total | 766 | 169 | 91 | 6 | 1032 |

- Vendor will purchase and install Projection Screens (approx 862)

  - 767 classrooms

  - 95 portables

- Vendor will purchase and install Ceiling Mounting for district owned projectors. Vendor will install district owned standard throw projectors and vendor will provide and install rapid-run cabling between projectors and presentation station (approx 170).

  - 153 classrooms

  - 15 classrooms requiring surface mount raceway

  - 1 portables

  - 1 portables requiring surface mount raceway

- Purchase and installation of Surge Protectors between projectors and presentation station (approx 1032)

- Removal and inventory of existing Television mounts (approx 168)

- Removal and inventory of existing Televisions (approx 911)

LCISD has defined specific Goals, Objectives and Strategies within their current Technology plan requiring Projectors to support Teaching and Learning, Promoting Educator’s and Staff Effectiveness and establishing supportable technology infrastructure.